## Slide 1
Research Overview
by
Shayan Taheri
University of Central Florida
Orlando, Florida
Fall 2015

## Slide 2
Choosing Algorithms for Desired Mathematical Operations
Implementing the Primitive Field Operations 2
Selecting the Type of Coordinates for Representing the Elliptic Points
Implementing Point Addition and Point Doubling
Implementing Point Multiplication
Defining Main Parameters and Rules for ECC Operation 1
ECC Hardware/Software – Level Implementation
This procedure can be
implemented using VHDL
or C++ language depending
on the type of implementation.

## Slide 3
Using A Computer Architecture Simulator
(e.g. Gem5 or HASE)
Running the Executable Files of the Implemented Algorithms on the Processor
Selecting A General-Purpose Processor 3
ECC Software – Level Evaluation
Memory Requirement Report
Running Time Report
Instructions Per Cycle Report

## Slide 4
Implementing Supplementary Hardware Blocks 4
ECC Hardware – Level Implementation and Evaluation
Constructing the Main Hardware Description File
Synthesis
(e.g. Synopsys Design Compiler)
Simulation
(e.g. Cadence NCSim or
Mentor ModelSim)
Power Extraction
(e.g. Synopsys Prime Time)
Temperature Extraction
(e.g. HotSpot)
Floorplanning and Routing
(e.g. Cadence SoC Encounter)
Testing and Verification
(e.g. Synopsys TetraMAX)
Area and Delay Report
Power Report
Temperature Report
Detectable Faults Report

## Slide 5
Comments
1. Example for Main Parameters  Finite Field, Elliptic Curve, Order of Field, and etc.
2. Example for Primitive Field Operations  Addition, Multiplication, Inversion, Squaring, and Division.
3. The instruction set architecture (ISA) of the processor can be modified in order to improve
the performance. Modification can be done by either adding or modifying instructions.
4. Example for Supplementary Hardware Blocks  Interface, Storage, Parameter Generation,
Arithmetic Logic Unit (ALU), Control, Security Scheme

## Slide 6
Designing Hardware Trojan Horse Functionality
Hardware Trojan Horse Injection and Its Footprint Evaluation
Targeting ECC Hardware-Level Implementation
Targeting ECC Software-Level Implementation
Performance Evaluation using
a Computer Architecture Simulator (e.g. Gem5 or HASE)
Injecting the Trojan in
a General-Purpose Processor
Footprint Evaluation using
an RTL Generation Tool
(e.g. FabScalar or AnyCore)
Injecting the Trojan in
an ECC Hardware
Footprint Evaluation based on
Hardware Evaluation Method (Refer to Page 4)
Performance Evaluation using
Field Programmable Gate Array
(i.e. Getting Running Time)